## Slide 1: Analyzing Security Vulnerabilities and Developing Defense Mechanisms in Vehicular Ad Hoc Networks (VANET)
GRADUATION PROJECT (1)
Students
ريم رامي بعاج
عدنان صبري
Supervisors
وسيم جنيدي
محمد يامن حلاق
1 / 9

## Slide 2: Project Objective and Previous Stages
Objective
Study and simulate the VANET network and its surrounding security threats, carry out a specific attack, and develop a defense mechanism
Proposed attacks for this semester: Black hole and Jamming
Completed in the Semester Project
Preparing the VANET environment
Creating an IP Spoofing attack, detecting it, and devising a mechanism to counter it
2 / 9

## Slide 3: Literature Review (1/2): Comparison Table
Publisher / Journal | Year | Study | What it covered | Research gap | Comparison with our project
Inderscience, Int. J. Vehicle Information and Communication Systems | 2025 | Performance Analysis of AODV-Based VANETs in Guwahati City: A Comparative Study of Propagation Models [1] | AODV baseline in a city scenario (SUMO + NS-3) with different propagation models | No attacks or security evaluation | Used as our no-attack baseline; we add attacks on top of it
Jurnal Online Informatika (JOIN) | 2025 | Performance Evaluation of Vehicular Ad Hoc Networks Considering Malicious Node Impact on Quality of Services Metrics [2] | Black hole and wormhole impact on QoS; black hole raised packet loss from 29% to 59% | Measures the impact only; no detection or defense | Same SUMO + NS-3 setup; we also build a detection method
Springer, EURASIP J. Wireless Communications and Networking | 2025 | Discovering Authentic Routes Using a Cryptographic Approach Against Blackhole Attack [3] | Cryptographic authentication of RREQ/RREP in AODV; PDR of 57.5%–81.82% (40–100 nodes) | Prevention only; adds cryptographic overhead | Behavioral detection from packet traces, without key management
3 / 9

## Slide 4: Literature Review (2/2): Comparison Table and Research Gap
Publisher / Journal | Year | Study | What it covered | Research gap | Comparison with our project
Int. J. Innovative Research and Scientific Studies | 2025 | GAN-Augmented Adversarial Training for Robust Detection of Complex Jamming Attacks in VANET Intelligent Systems [4] | GAN-augmented CNN–Random Forest jamming detection; 93.4% F1-score | Jamming only; focuses on the detection model | We simulate jamming and measure its impact on the network
Int. J. Intelligent Engineering and Systems (IJIES) | 2025 | Leveraging DenseNet-ABiLSTM for Effective Jamming Attack Detection in VANETs [5] | DenseNet-ABiLSTM jamming detection; 98.7% binary accuracy | Jamming only; dataset-based deep learning | We combine jamming and black hole in one simulated VANET
Research gap
Existing studies each cover only one piece: attack-free baselines [1], impact measurement without defense [2], prevention that adds cryptographic overhead [3], and dataset-based jamming detection without a simulated network evaluation [4][5]. None combines attack simulation, detection and a defense mechanism in one realistic SUMO + NS-3 VANET scenario.
Goal
Simulate Black hole and Jamming attacks in a realistic SUMO + NS-3 VANET, then develop and evaluate a detection and defense mechanism against them.
4 / 9

## Slide 5: Implementation Phases and Tools
1
Scenario design
Real city map and traffic density/speed in SUMO
2
Normal case
Run without attacks and extract KPIs (delay, packet loss)
3
Jamming
Physical-layer attack simulation
4
Black hole
Network-layer routing attack involving malicious packet dropping and potentially forged AODV route replies
5
Developing and evaluating the security solution
Design the defense mechanism and measure its effect on network performance
Tools used
SUMO
Traffic mobility
NS-3
Network simulation
Python + TraCI
Integration and visualization
Ubuntu on VMware
Platform
5 / 9

## Slide 6: Proposed Network Topology and AODV Header
AODV RREQ header (32 bits per row)
Type = 1
J R G D U
Reserved
Hop Count
RREQ ID
Destination IP Address
Destination Sequence Number
Originator IP Address
Originator Sequence Number
AODV RREP header
Type = 2
R A
Reserved
Prefix Sz
Hop Count
Destination IP Address
Destination Sequence Number
◄ Black hole
Originator IP Address
Lifetime
a forged RREP advertises an inflated Destination Sequence Number (highlighted) to attract the route, then Vehicle 20 drops the packets [6]
no AODV header field is changed; the attacker interferes with the radio channel, so RREQ, RREP and data packets are corrupted or lost
6 / 9

## Slide 7: Experimental Results
Network Performance Under Attack
Metric | Normal | Under Attack
Sent Packets | 42 | 42
Received Packets | 36 | 25
PDR | 85.71% | 59.52%
Packet Loss | 6 | 17
Throughput | 0.6588 Kbps | 0.451 Kbps
Average Delay | 59.39 ms | 58.20 ms
7 / 9

## Slide 8: Where We Stopped and What Continues
We stopped at: Black Hole stage 1 (malicious packet dropping) with offline detection
Continuing now: forged RREP, then physical-layer Jamming
Completed
VANET simulation with 40 vehicles and 2 RSUs using NS-3 and SUMO
AODV-based multi-hop network simulation
Security solution evaluation
Malicious packet-dropping implementation
Offline behavioral Black Hole detection using packet reception and forwarding traces
Detection evaluation under different attacker configurations
SUMO visualization of the malicious vehicle
Continuing Now (Future Work)
Complete Black Hole attack using forged RREP messages
Implement physical-layer Jamming attack
Extend detection evaluation across more scenarios
Improve real-time attack detection and mitigation
8 / 9

## Slide 9: References
[1] R. J. Borah and D. Ganga, “Performance analysis of AODV-based VANETs in Guwahati city: a comparative study of propagation models,” Int. J. Vehicle Information and Communication Systems, vol. 10, no. 1, pp. 61–84, 2025.
[2] N. F. Alfarizi, M. T. Nuruzzaman, S. Uyun, B. Sugiantoro, and M. F. A. bin Abdullah, “Performance Evaluation of Vehicular Ad Hoc Networks Considering Malicious Node Impact on Quality of Services Metrics,” Jurnal Online Informatika, vol. 10, no. 2, pp. 299–307, 2025.
[3] M. Ghute and Y. Suryawanshi, “Discovering authentic routes using a cryptographic approach against blackhole attack,” EURASIP J. Wireless Commun. Netw., vol. 2025, Art. no. 86, 2025.
[4] N. A. K. Zghair, W. K. Jawad, J. J. Alwash, M. A. Almaiah, and R. Shehab, “GAN-augmented adversarial training for robust detection of complex jamming attacks in VANET intelligent systems,” Int. J. Innovative Research and Scientific Studies, vol. 8, no. 3, pp. 4304–4314, 2025.
[5] A. S. Srinivas T et al., “Leveraging DenseNet-ABiLSTM for Effective Jamming Attack Detection in VANETs: A Hybrid Model with DRA-driven Feature Optimization,” Int. J. Intelligent Engineering and Systems, vol. 18, no. 11, 2025.
[6] C. Perkins, E. Belding-Royer, and S. Das, “Ad hoc On-Demand Distance Vector (AODV) Routing,” RFC 3561, IETF, Jul. 2003.
9 / 9